## Slide 1
Close the loop in CDS in 10 steps
Ammar Al-Jodah

## Slide 2: Content
IOP and open loop mdl file
Build, install, start of realtime code local_dc start
diaggui step response
diaggui find transfer function
Matlab, Simulink control system design and simulation
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Foton, define the controller filter
Closed loop mdl file
Build, install, start of realtime code local_dc start
diaggui step response
Step 10
Step 9
Step 7
Step 8
Export data to matlab, find the transfer function equation

## Slide 3: Software used
Ndscope
diaggui
Foton

## Slide 4: Hardware used
FE and Extension box holds the Cards: ADC, DAC on a PCIe bus
RC circuit

## Slide 5: RC circuit theoretical modelling
Vi
Vo
R1
R2
C

## Slide 6: RC circuit theoretical modelling
Vi
Vo
R1
R2
C

## Slide 7: RC circuit theoretical modelling
Vi
Vo
R1
R2
C

## Slide 8: Open-loop simulation
clc;close all;clear all
data = sim('open_loop_sim.slx')
r = ones(length(data.t)).*5;
plot(data.t,r, data.t, data.y, 'linewidth',2)
grid
xlabel('time (s)')
ylabel('Vo (v)')
legend('reference', 'actual')
ylim([0 6])
openloop_step.m
open_loop_sim.slx

## Slide 9: Open-loop simulation
Open-loop frequency step response

## Slide 10: Open-loop simulation
Open-loop transfer function
close all;clear all;clc
f = logspace(-2,0,10);
G = tf([1], [1 2])
[mag1, pha1] = bode(G,2*pi*f); semilogx(f,20*log10(squeeze(mag1)), 'linewidth',2)
xlim([0.01 1]);grid
xlabel('frequency (Hz)')
ylabel('Magnitude (db)')
openloop_freq_resp.m

## Slide 11: Step 1: IOP and open loop mdl
IOP stored at /opt/rtcds/usercode

## Slide 12: Step 1: IOP and open loop mdl
Open loop

## Slide 13: Step 2: Build, install, start IOP, and Openloop mdl
Build + Install
$ rtcds build u2iop
$ rtcds install u2iop
$ rtcds build u2rcsys
$ rtcds install u2rcsys

## Slide 14: Step 2: Build, install, start IOP, and Openloop mdl
Change master file
$ sudo nano /etc/advligorts/master
Add the following
/opt/rtcds/uwa/u2/chans/daq/U2IOP.ini
/opt/rtcds/uwa/u2/chans/daq/U2RCSYS.ini
/opt/rtcds/uwa/u2/target/gds/param/tpchn_u2iop.par
/opt/rtcds/uwa/u2/target/gds/param/tpchn_u2rcsys.par
ctrl+o, enter, ctrl+x

## Slide 15: Step 2: Build, install, start IOP, and Openloop mdl
Change test point file
$ sudo nano /etc/advligorts/testpoint.par
Add the following
[U-node12]
hostname=u2fe1
system=u2rcsys
[U-node78]
hostname=u2fe1
system=u21iop
ctrl+o, enter, ctrl+x

## Slide 16: Step 2: Build, install, start IOP, and Openloop mdl
Start models and local dc
$ rtcds start u2iop
$ rtcds start u2rcsys
$ local_dc -s u2rcsys -d /opt/rtcds/uwa/u2/target/gds/param/
If more than one model to be run, you need to put their names here

## Slide 17: Step 2: Build, install, start IOP, and Openloop mdl
Open Global Diagnostics Screen (GDS)
$ cd /opt/rtcds/uwa/u2/medm/u2iop
$ medm U2IOP_GDS_TP.adl

## Slide 18: Step 2: Build, install, start IOP, and Openloop mdl
Open U2RCSYS Global Diagnostics Screen (GDS)
$ cd /opt/rtcds/uwa/u2/medm/u2rcsys
$ medm U2RCSYS_GDS_TP.adl

## Slide 19: Step 2: Build, install, start IOP, and Openloop mdl
Start ndscope
$ NDSSERVER=u2fe1:8088 ndscope
Select the channels

## Slide 20: Step 3: diaggui: open-loop step response
Start diaggui
$ NDSSERVER=u2fe1:8088 LIGO_RT_BCAST=u2fe1 diaggui -v

## Slide 21: Step 3: diaggui: open-loop step response

## Slide 22: Step 3: diaggui: open-loop step response

## Slide 23: Step 4: diaggui: finding transfer function
Start diaggui
$ NDSSERVER=u2fe1:8088 LIGO_RT_BCAST=u2fe1 diaggui -v

## Slide 24: Step 4: diaggui: finding transfer function
Select the measurement signal
Set Swept sine settings

## Slide 25: Step 4: diaggui: finding transfer function
Select the excitation signal
Set the amplitude

## Slide 26: Step 4: diaggui: finding transfer function
Start
Export results

## Slide 27: Step 5: sysident: transfer function fitting
Exported data
0.0099999998 -6.0167427 -2.1172364
0.016681006 -6.0351129 -3.5013008
0.027825594 -6.0723886 -5.7871747
0.046415888 -6.1603427 -9.5233917
0.077426367 -6.38203 -15.495438
0.12915497 -6.9235191 -24.538395
0.21544346 -8.1057043 -36.789986
0.35938138 -10.248335 -50.551247
0.59948426 -13.35558 -62.882248
1 -17.113218 -72.070374
Plot with experimental transfer function with the model

## Slide 28: Step 5: sysident: transfer function fitting
Matlab code to plot
clc;close all;clear all
file_name = 'data.txt';
data = importdata(file_name);
f = data(:,1);
mag2 = data(:,2);
pha2 = data(:,3);
G = tf([1], [1 2])
[mag1, pha1] = bode(G,2*pi*f);
figure(1)
semilogx(f,20*log10(squeeze(mag1)), 'linewidth',2)
xlim([0.01 1])
grid
hold on
semilogx(f,mag2, 'linewidth',2)
legend('model', 'experiment')
xlabel('frequency (Hz)')
ylabel('Magnitude (db)')
figure(2)
semilogx(f,squeeze(pha1), 'linewidth',2)
xlim([0.01 1])
grid
hold on
semilogx(f,pha2, 'linewidth',2)
legend('model', 'experiment')
xlabel('frequency (Hz)')
ylabel('Phase (deg)’)
mag_abs = 10.^(mag2/20);
w = 2*pi*f;
T = 1/16384;
compare_theoretical_model_exp.m
Used for the sysident

## Slide 29: Step 5: sysident: transfer function fitting
Setup sysident to fit the transfer function

## Slide 30: Step 5: sysident: transfer function fitting
Comparing the results
compare_fit_model_exp.m

## Slide 31: Step 6: Matlab, Simulink: controller design

## Slide 32: Step 7: closed-loop mdl

## Slide 33: Step 8: Build, install, start IOP, and Openloop mdl
Same as step 2 but the local dc should have the new model name
$ local_dc -s u2rccl -d /opt/rtcds/uwa/u2/target/gds/param/
If you want to have the closed loop model on the same node then you need to edit the file /opt/rtcds/uwa/u2/target/gds/param/testpoint.par and remove the old model at the same node number

## Slide 34: Step 9: Foton: filter design
/opt/rtcds/uwa/u2/chans

## Slide 35: Step 10: diaggui: closed-loop step response

## Slide 36: Step 10: diaggui: closed-loop step response

## Slide 37: Thank you